## Slide 1: AI Testbench Studio
From RTL to verified, with an AI that debugs itself.
ForgeHacks 2026 | Track: AI + Education
Notes: Hi, I'm [name]. This is AI Testbench Studio, built for ForgeHacks 2026 in the AI plus Education track.

## Slide 2: The problem: verification is hard to learn
Testbenches are hard
Writing one takes as long as the design: timing, reference models, tool flags.
Failures are confusing
When a simulation fails, beginners cannot tell if the testbench or the RTL is wrong.
So it gets skipped
Students and hobbyists ship unverified hardware and miss the habits that matter.
Who it hurts: digital-design students, FPGA / RISC-V hobbyists, instructors.
Notes: Writing a testbench takes as long as writing the design. And when a simulation fails, beginners cannot tell who is wrong, the testbench or their Verilog. So many students skip verification altogether.

## Slide 3: The solution: an AI verification partner
Upload RTL
Verilog or SystemVerilog file
AI writes testbench
Self-checking, with corner cases
Real simulation
Icarus Verilog compiles and runs it
AI explains failures
Testbench error or real RTL bug
The AI's work is checked by a real simulator, never trusted blindly.
Notes: AI Testbench Studio fixes that. Upload RTL, an LLM writes a self-checking testbench, Icarus Verilog compiles and simulates it, the AI repairs compile errors, and if checks fail it tells you whether the testbench or your design is at fault.

## Slide 4: How it works
RTL file
>
LLM writes tb.v
>
iverilog compile
>
vvp simulate
>
Verdict
Loop 1: compile errors
Errors go back to the AI, which repairs the testbench automatically (configurable retries).
Loop 2: failing checks
AI decides TB_ERROR (fixes testbench) or RTL_BUG (explains your design's bug).
Notes: The pipeline: upload, generate, compile, simulate, verdict. Two feedback loops: compile errors are sent back to the AI, and failing checks trigger a verdict on whether the testbench or the RTL is wrong.

## Slide 5: Live demo
1. Pass
alu8.v: AI writes the testbench, simulation runs, all checks passed.
2. Catch
Decade counter that wraps at 10 instead of 9: AI verdict is RTL bug, with explanation.
3. Inspect
One click opens GTKWave with the signals already listed.
Switch to the app now.
Notes: Switch to the app. Demo 1: alu8, all checks pass. Demo 2: buggy decade counter, the AI reports an RTL bug. Demo 3: open the waveform.

## Slide 6: Technical components
LLM backends
Gemini, Groq, Hugging Face, OpenRouter, local Ollama
Prompt engineering
Strict testbench rules, timing and reference-model guidance
Closed-loop tooling
iverilog and vvp results drive repair prompts
Verdict reasoning
TB_ERROR vs RTL_BUG, conservative about blaming RTL
Sanity guards
Catches t=0 runs, watchdog hits, and zero checks
Python + Tkinter
Standard library only, plus GTKWave integration
Notes: Under the hood: provider-agnostic LLM backends, strict prompt engineering, closed-loop tool use with Icarus Verilog, verdict reasoning, and guards against false passes.

## Slide 7: Real-world impact
Students
A working testbench, live results, and plain-English failure explanations teach verification habits.
Small teams
Removes testbench boilerplate for FPGA and open-source RISC-V projects.
Classrooms
Free-tier and fully offline options work with low budgets and poor connectivity.
Trustworthy by design: a real simulator checks the AI.
Notes: It is free to run, works offline, and the AI's work is checked by a real simulator rather than trusted blindly.

## Slide 8: Thank you
GitHub: <your-repo-url>
Video: <your-youtube-url>
AI Testbench Studio | ForgeHacks 2026 | AI + Education
Notes: Built for ForgeHacks, AI plus Education. The code is on GitHub. Thanks for watching.